## Slide 1: Arduino Microcontroller for a model Hen-House

## Slide 2: Kit* Materials
Arduino Microcontroller – SparkFun RedBoard
Breadboard
Arduino and breadboard holder
USB Mini-B Cable
Wall adapter power supply
Resistors – not used in this example
3mm LEDs in assorted colors
Jumper wires in assorted colors
Test leads – alligator clip with pigtail in assorted colors
Screwdriver
Computer (Windows, Mac OS X, or Linux) – not included
Arduino Software – not included
*Arduino Microcontroller Kit, available from agclassroomstore.com.

## Slide 3: new to working with Arduino?
Learn about the SparkFun RedBoard
https://learn.sparkfun.com/tutorials/redboard-hookup-guide?_ga=2.253854920.1963503614.1546674686-1301118510.1532554968
And other Arduino microcontrollers
https://www.arduino.cc/en/Guide/HomePage
https://www.tinkercad.com/
https://learn.adafruit.com/category/learn-arduino
https://www.instructables.com/class/Arduino-Class/
http://www.ladyada.net/learn/arduino/
https://www.youtube.com

## Slide 4: THIS EXAMPLE USES A SIMPLE BLINK PROGRAM TO CONTROL THE LIGHTS AND FANS ON A MODEL HEN HOUSE.

## Slide 5: ATTACH THE BREADBOARD AND ARDUINO REDBOARD TO THE BLACK HOLDER.

## Slide 6: Program the Arduino

## Slide 7: download Arduino IDE HTTPS://WWW.ARDUINO.CC/EN/MAIN/SOFTWARE

## Slide 8: start a new program File> New

## Slide 9: Select the Type of Arduino Board You are using tools > Board >Arduino AVR Boards> Arduino Uno

## Slide 10: Write a Program the example program is a simple blink program with three outputs.

## Slide 11: Verify the program by clicking on the button with a checkmark

## Slide 12: Connect the microcontroller to the computer Using the red USB Mini-B Cable tools> Port> USB serial port

## Slide 13: Upload the program to the RedBoard Disconnect the Redboard from the computer

## Slide 14
USE JUMPER WIRES TO CONNECT THE ARDUINO TO THE BREADBOARD.
THE GREEN WIRE CONNECTS PIN 2 TO HOLE J2.
THE BLUE WIRE CONNECTS
PIN 4 TO HOLE J4.
THE RED WIRE CONNECTS
PIN 6 TO HOLE J6.
THE BLACK WIRE CONNECTS THE GROUND PIN (GND) TO THE NEGATIVE RAIL ON THE LEFT SIDE OF THE BREADBOARD.

## Slide 15
PLACE TEST LEADS WITH ALLIGATOR CLIPS IN THE BREAD BOARD.
ADD TEST LEADS TO HOLES F2, F4, AND F6. THESE TEST LEADS CARRY A POSITIVE CHARGE.
ADD TEST LEADS TO THE THE NEGATIVE RAIL ON THE LEFT SIDE OF THE BREADBOARD. THESE TEST LEADS CARRY A NEGATIVE CHARGE.

## Slide 16
CONNECT THE TEST LEADS TO THE HEN HOUSE. POSITIVE TO POSITIVE. NEGATIVE TO NEGATIVE. PIN 2 AND PIN 4 WILL CONTROL LIGHTS AND PIN 6 WILL CONTROL THE FAN.
Positive
Negative

## Slide 17
ADD POWER TO THE ARDUINO.
ONCE THE ARDUINO HAS POWER THE HEN HOUSE LIGHTS AND FANS WILL TURN ON AND OFF.